BUILDING BYELAWS

DEFENCE HOUSING AUTHORITY

ISLAMABAD/RAWALPINDI

REVISED 2016

TABLE OF CONTENTS

| Contents |  | Page |
| --- | --- | --- |
| Chapter – I | Preliminary | 1 |
| 1. | Authority | 1 |
| 2. | Definitions | 1 |
| 3. | Application of Byelaws | 6 |
| 4. | Exemptions | 6 |
| 5. | Interpretation of Byelaws | 6 |
| Chapter – II | General Regulations | 7 |
| 1. | General | 7 |
| 2. | Corner Plot | 7 |
| 3. | Over / Under Size Plot | 7 |
| 4. | Annexation of Adjacent Extra / Trapped Land | 7 |
| 5. | Sub-Division of Plots | 7 |
| 6. | Amalgamation of Plots | 8 |
| 7. | Leveling of Plots | 8 |
| 8. | Chamfering of Corner | 8 |
| 9. | Services | 8 |
| 10. | Water Supply | 8 |
| 11. | Sewerage / Manhole | 9 |
| 12. | Gas / Telephone / Electric | 10 |
| 13. | Damages | 10 |
| 14. | Bearing Capacity Test | 10 |
| 15. | Termite Proofing | 10 |
| 16. | Blockage of Street | 10 |
| 17. | Lighting and Ventilation | 10 |
| 18. | Blasting | 12 |
| 19. | Disputes | 12 |
| 20. | Possession of Plots | 12 |
| 21. | Preparation of Building Plans | 13 |
| 22. | Submission of Drawings | 13 |
| 23. | Approval of Submission Drawing | 14 |
| 24. | Revised Submission Drawing | 15 |
| 25. | Revalidation of Submission Drawing | 15 |
| 26. | Oversight in Scrutiny of Drawings | 15 |
| 27. | Demarcation of Plot | 15 |

| 28. | SOP for Demarcation Check | 15 |
| --- | --- | --- |
| 29. | Approved Drawings | 16 |
| 30. | Inspection During Construction | 16 |
| 31. | Addition / Alteration | 17 |
| 32. | Construction without Approval | 17 |
| 33. | Duplicate Copy of Documents | 17 |
| 34. | Completion Plan | 17 |
| 35. | Revised Completion Plan | 18 |
| 36. | Cancellation of Completion Plan | 18 |
| 37. | Imposition of Utility Bills | 18 |
| Chapter – III | Space Requirement for Building | 19 |
| 1. | Residential Building Standards | 19 |
| 2. | General Conditions | 19 |
| 3. | Commercial Building Standards | 34 |
| 4. | General Condition for Commercial | 34 |
| Chapter – IV | Health and Safety Guidelines | 45 |
| Chapter – V | Administrative Aspects | 46 |
| Chapter – VI | Construction Byelaws | 48 |
| Annexes | a. Specimen Drawing - Annex-A | 50 |
|  | b. Fines - Annex-B | 51 |

CHAPTER-I

PRELIMINARY

## 1.	Authority

a.	This Regulation may be called “DHA Islamabad-Rawalpindi Building Control Regulation 2000 (Revised 2016)” made by the Executive Board in exercise of the powers conferred by the Section 20 of The Gazette of Pakistan, Part-I, Act No XII of 2013.

b.	It extends to all residential and commercial plots / buildings in the DHA Islamabad-Rawalpindi (DHAI-R).

c.	These Byelaws supersede all the previously published Byelaws.

d.	They shall come into force with effect from January 2016.

e.	The DHAI-R is empowered to change or make amendments in these regulations as and when required.

## 2.		Definitions.In this regulation and in the subsidiary instructions that may be issued from time to time, frequently referred terms have the meanings as indicated. Where any term is not defined, it shall have ordinary meanings or such as the context may apply.

a.		Act and Regulation. The “Act” means DHAI-R Act 2013 and ‘Regulations’ means regulations made under this Act.

b.		Addition / Alteration / Revision in Plan. Means changes in already existing building or in approved building plan.

c.	Amenity Plot. Plot allocated exclusively for the purpose of amenity uses, such as government offices, health, welfare, education, worship places, burial grounds, parking and recreational areas.

d.	Amalgamation. The joining of two or more adjoining plots into a single plot in accordance with these Byelaws.

## e.	Ancillary Building. Means a building subservient to the principal building on the same plot e.g servant quarters, garages etc.

## f.	Apartment. Means an independent residential unit in a building consisting of at least one bedroom, a living room, a bathroom, a kitchenette and a store.

g.	Arcade. A covered walk-way or a verandah between the shops and the road or street on which the shops abut.

h.	Area. Means the area under jurisdiction of the DHAI-R and / or the area shown in the Master Plan of DHAI-R and including any extension or modification affected therein from time to time.

j.	Balcony. Means an outside projection from a building overlooking a compound, road or courtyard and projecting in front of a room and not used for sitting purpose.

## k.	Basement. Means a structure wholly or partly below natural ground level / approach road level.

l.	Building / House Line. Means a line beyond which the outer faces of any building except boundary wall, porch and projection may not extend.

m.	Building Works. Means site excavation, erection or re-erection of a building or making addition / alteration to existing building.

n.	Building Plan. Means a plan showing detailed arrangements for intended building to be constructed on allotted plot.

o.	Byelaws. Means the laws and regulations approved by Executive Board / Competent Authority of DHAI-R.

p.	Carpet Area. The net floor area within a habitable, rent-able or saleable unit excluding the area of peripheral walls but including the area of internal walls and columns.

q.	Corner plot. Means a plot situated at the intersection of two vehicular streets.

### r.	Commercial Area. Means the area where shops, show-rooms, stores / godowns, ware-houses, other market centres, hotels, clubs, petrol and gas filling stations etc are to be constructed.

### s.	Commercial Building. Means a building having shops, show rooms, offices, hotels, restaurant or apartments.

t.	Competent Authority. Means President / Vice President, Administrator of 
DHAI-R or concerned officer empowered by the Authority to approve the plans and to control building activity.

u.	Covered Area. Means (for the purpose of determining the floor area) the sum of the gross horizontal areas of the floor / floors, including, verandas, 25 percent of the area covered by pergolas but excluding shades / projections (not exceeding the maximum permissible limits).

v.	Existing Building. Mean a building already existing on the ground on the date of commencement of alteration / addition plan.

w.	Extra Land. Any piece of land that has been left vacant adjacent to any plot / s would be the property of DHAI-R which reserves the right to allot it to any member on payment or keep it for its own use.

### x.	Flats. Mean block / blocks of buildings consisting of a number of residential units built in a horizontal or vertical manner exclusively designed for human habitation in the Residential / Commercial Area.

y.	Floor Area Ratio. (FAR) Means the total covered area of a building or buildings on a plot divided by the total area of that plot.

z.	Footprint. The portion of a plot of land covered at any level by a building or part thereof other than basement.

aa.	Foundation. Means a RCC structure designed to bear and distribute the load of 	building into the ground through RCC columns, pillars, beams or walls.

bb.	Frontage of Corner Plot. Frontage of plots opening on more than one road will be with reference to the street no as per the possession / site plan.

cc.	Height of Building. Shall be taken as vertical measurement from the crown of front approach road to the highest part of building.

dd.	Licensed Architect.  Means a person registered with Pakistan Council of Architects and Town Planners (PCATP) and on panel of DHAI-R.

ee.	Licensed Engineer. Means a person registered with Pakistan Engineering Council (PEC).

ff.	Master Plan. Means the plan showing layout of the area with schedule and supported by written statement of goals and objectives and financial implications.

gg.	Mumty. A structure with a covering roof over a primary (main) or secondary staircase and its landing built to enclose the stairs for the purpose of providing protection from weather.

hh.	Non-Conforming Use. Means the use of a plot or structure thereon not conforming to the purpose authorised or permitted under this regulation.

jj.	Open Stairs Case. Means a stairs case of which the roof must be fully open to the sky or without RCC roof and of which at least two sides must be fully open and clear of any adjoining walls of any other building.

kk.	Pergola. Means a structure of which the roof must be at least 75 percent open to sky.

ll.	Party Wall. Means a common wall between two adjacent buildings on independent plots.

mm.	Parapet. Means a wall, whether plain, perforated or panelled, protecting the edge of a roof, balcony, veranda or terrace.

nn.	Plinth. The height of finished floor level of the ground floor, measured from the top of finished surface of the road serving the plot, taken from the centre of the property line of the plot along the road. In case of more than one road serving the plot, the plinth will be measured from the reference road providing principal access.

oo.	Projection. Means an outer side projection from the building line to provide protection from weather and sun.

pp.	Property Line. Boundary line of plot which separates private property from the public property or a private property from another private property.

qq.	Possession. Means handing over of a demarcated plot to the member with demarcation of four corners.

rr.	Public Buildings. Means a building designed for public use such as hospital / dispensary, post office, police station, town hall, library, recreational buildings and club etc.

ss.	Residential Building. Means a building authorised for residential occupancy by one or more families.

tt.	Residential Plot. Means a plot allotted exclusively for residential purpose.

uu.	Set-back / Compulsory Open Space.  Means a space compulsorily required to be left open between the building and the plot line without any obstruction.

vv.	Storey. Means the space between the floor and the ceiling of a building.

ww.	Structural Alteration. Means any change in the structure of a building i.e supporting members of a building such as load bearing walls, columns, beams, slabs etc.

xx.	Shop–Cum-Flats.  Means provision of shops on the ground floor and flats  / offices on the subsequent floors in commercial area.

yy.	Sector Shops / Convenient Stores. Means a row of shops in residential area for routine utility requirements.

zz.	Stores / Godowns. Means a building / buildings meant for storage of material. Those goods are not of inflammable or objectionable character.

aaa.	Septic Tank. Means a tank in which sewage is collected and decomposed before its discharge into a public sewer or Soakage Pit.

bbb.	Soakage Pit. Means a pit filled with aggregate, boulders or broken bricks and intended for the reception of wastewater or effluent discharged from a Septic Tank.

ccc.	Trapped Land. Land which is not accessible / approachable by the Authority.

ddd.	TP&BC Directorate. Town Planning & Building Control Directorate.

3.	Application of Byelaws

a.	Every person who, within the limits of DHAI-R, intends to carry out addition or alteration to existing building or demolish the existing building or erects or re-erects a building shall comply with the requirement of these Byelaws.

b.	A building plan shall be approved only for the specified purpose of the plot mentioned in allotment letter.

## 4.	Exemptions.	Application of these Byelaws can be relaxed by Competent Authority provided there is sound justification from engineering, town planning, architecture and all other relevant aspects.

## 5.	Interpretation of Byelaws.	In case of any ambiguity in interpretation of any Byelaws, 
DHAI-R reserves the right to deliver / implement the interpreted contents of such Byelaws.

#### CHAPTER-II

# GENERAL REGULATIONS

1.	General. These regulations have been framed with a view to facilitate construction by the members. Due relaxation has been ensured while specifying covered area and other details. The designers have been extended leverage to contribute such designs which add to the overall complexion of a healthy environment / development:-

a.	Any one who intends to carry out building works within the boundary of DHAI-R should strictly comply with the requirement of these BYELAWS.

b.	The plot shall be strictly utilized for the purpose it has been allotted. To preserve the sanctity of planning, NO DEVIATION SHALL BE PERMITTED.

2.	Corner Plot. The owner of corner plot will be required to pay additional (10% of original total) cost as laid down by DHAI-R.

3.	Over / Under Size Plots. Plots measuring less area as compared to standard size plot will be remitted cost of land only. Similarly those, measuring more than the standard size plot shall be required to pay for the extra / additional area as per the rates decided by DHAI-R.

4.	Annexation of Adjacent Extra / Trapped Land. In case where extra land is available adjacent to the plot, it may be purchased by the member. Rates and permission of such cases is subject to approval by DHAI-R. Construction on extra land is not allowed without changing its category to constructable.

5.	Sub-Division of Plots

a.	Residential. Sub-division is not allowed for 500 sq yds and below cat plots however 1000 sq yds plots can be divided into two units provided 1000 sq yds plots lies in the line with 500 sq yds plots after payment of dues as per DHAI-R policy. Amalgamated plot can be subdivided into two separate plots provided the construction is done according to the Byelaws of smaller plot, after payment of dues as per DHAI-R policy.

b.	Commercial. Sub-division is not allowed.

6.	Amalgamation of Two Plots. With specific permission, adjacent plots / land may be combined together to form a single unit upto maximum of 4 kanals (residential) including extra land (any category) provided entire piece of land has single ownership. Such unit when constructed will not be sub-divided unless complete building is dismantled. Such amalgamated plot / land including green area will be governed by applicable DHAI-R Building Byelaws.

7.	Levelling of Plots. In case of any abnormality in the plot such as ditch or mound etc, DHAI-R will not be responsible for any protective work or development within the plot line. However if adjacent plot/s are at higher level from the reference road, the member can excavate the adjacent plot upto reference road level for construction and the safety of boundary wall. Excavation in adjacent plot below the reference road level will not be permitted.

8.		Chamfering of Corner. For smooth flow of traffic at turning, the corner of a plot bounded by two roads shall be tapered / chamfered by a standard i.e 6 ft x 6 ft on either side from the corner for all categories except commercial plots.

9.		Services. The DHAI-R will provide roads including all services and the members are required to plan extension of these services to their buildings accordingly. Further extension of the services to other users is strictly disallowed. Defaulting members are liable to disconnection of services and financial penalties.

10.		Water Supply

a.	Application for water connection shall be made on the prescribed form to the DHAI-R.

b.	No person is permitted to install motor / pump on the water supply line. Only one connection shall be provided for each building.

c.	Construction of under ground and overhead water tank is mandatory.

d.	Boring of any type for the purpose of water, sewerage, drainage etc is strictly prohibited in the territory of DHAI-R except where found necessary.

e.	Residential

(1)	No water point / tap will be left outside the boundary wall.

(2)	Construction of under ground water tank is mandatory but not on the slope side and be so located / designed that bowzer filling is facilitated.

(3)	Member found violating the instructions on water supply will be asked to pay violation charges as per DHAI-R policy.

(4)	Washing of car on the road is not allowed.

(5)	Flow of water through porch on the road is not allowed.

f.	Commercial

(1)	Separate water connection for all owners of flat in commercial building.

(2)	Over Head water tank must consist of two portions, one for fire fighting and other for storage purpose.

(3)	GI pipe of 2.5 dia should run from top to basement.

11.	Sewerage / Manhole. Byelaws regarding house connection to main sewer are as under:-

a.	WC discharge be connected with the DHAI-R manhole through septic tank.

b.	Wash room and kitchen drainage be connected direct to the over flow manhole of septic tank. It shall not be connected to the septic tank.

c.	Rain water / storm water be disposed off in open drains or on the adjacent roads as per design of the said Phase. It should not be connected to the sewer lines.

d.	Members are required to construct proper manholes and septic tanks (only RCC construction).

e.	Members are required to get their septic tanks inspected before covering their tops.

f.	Connection to the main sewer line shall be provided by DHAI-R on completion of house / building and member will not tamper with main sewer line. Defaulters will be charged as per DHAI-R policy issued from time to time.

g.	Where a resident / member excavates basement as per his requirement and decides to have bath rooms / toilets, the sewerage disposal will be through mechanical pumps by the resident.

12.		Gas / Telephone / Electric. The services have been laid by DHAI-R and individual connection to houses be obtained from respective departments in accordance with respective departmental regulations.

13.		Damages. No body is permitted to damage roads and services laid by DHAI-R. In case of extension of services, if any damage is likely to be caused to road, sewer line, rain water line etc such work shall not be undertaken without prior approval of DHAI-R. In case of damages, DHAI-R will impose penalties and cost of repair work will be recovered from member.

14.		Bearing Capacity Test. Bearing capacity tests will be arranged by the member through 
DHAI-R approved laboratory. The approved list is available in TP&BC Directorate.

15.		Termite Proofing. As there is a positive evidence of the presence of termite in 
DHAI-R, members will ensure termite-proofing treatment during construction stage.

16.		Blockage of Street

a.	No part of any street shall be used in connection with the construction, repair or demolition of any building without prior written permission of DHAI-R. Street will not be blocked under any circumstance.

b.	No excavation shall be made in any street for utility without prior permission from 
DHAI-R.

c.	Defaulters will have to pay charges as per DHAI-R Byelaws.

17.		Lighting and Ventilation

a.	Size of External Openings

(1)	Every room, other than rooms used predominantly for the storage of goods, shall be provided with natural light and natural ventilation by means of one or more openings in external walls. These openings shall have a combined area of not less than 10% for habitable rooms and 7.5% for other rooms of the floor space of such opening and the whole of such openings shall be capable of allowing free and uninterrupted passage of air.

(2)	Area for openings in case of warehouse, godown, storage places etc shall not be less than 5% of the floor space unless the space is mechanically ventilated.

b.	Size of Internal Openings. Unless the light and ventilation requirements are met by an air well or ventilation duct, all internal habitable rooms must have openings in internal air wells in addition to door openings not less than 7.5% of the floor area of such room. Access for maintenance of shaft be provided at level from where the shaft commence.

c.	Internal Air Wells

(1)	Habitable rooms may receive daylight and natural ventilation from internal air wells which shall conform with the following minimum sizes:-

(a)	For buildings upto 2 storeys, 20 sft with minimum width of well 5 ft.

(b)	For buildings with 3 to 5 storeys, 100 sft with minimum width of well 8 ft.

(c)	For buildings higher than 5 storeys, 100 sft plus 10 sft for each additional floor over storeys and minimum width of well 10 ft.

(2)	Where only kitchens, WC and bath rooms receive daylight and ventilation from air wells, their sizes shall conform with the following as minimum:-

(a)	For building upto 2 storeys, 25 sft with minimum width of well 3 ft.

(b)	For buildings with 3 to 5 storeys, 50 sft with minimum width of well 5 ft.

(c)	For building higher than 5 storeys, 50 sft plus 5 sft for each additional floor with minimum width of well 5 ft.

d.	Permanent Openings in Kitchen. Every kitchen shall have openings for permanent ventilation into the external air space not less than 15 % of its floor area.

e.	Water Closet, Bath Room & Ablution Places. Every water closet, urinal stall and bath room and ablution area shall be provided with natural lighting and ventilation by means of one or more openings in external walls having a combined area of not less than 2 sft per water closet, urinal or bath room except where adequate and permanent mechanical ventilation is provided and which discharges into an open space.

f.	Garages. Every garage shall be provided with opening of not less than 5% of the floor area for ventilation and lighting incorporated in a wall or in the door.

g.	Staircase. All staircases which are enclosed shall be provided with adequate lighting and ventilation from openings not less than 7.5% of the staircase area.

h.	Mechanical Ventilation & Central Air Conditioning Waiver-Minimum Requirement

(1)	Where undertaking for central air conditioning and permanent mechanical ventilation is provided, the relevant clauses of these regulations dealing with natural ventilation, lighting and heights of rooms may be waived.

(2)	Where permanent mechanical ventilation in respect of lavatories water closets, bath rooms or corridors has been provided, conditions relating to natural ventilation and natural lighting under these Regulations shall not apply to such lavatories water closets bath rooms or corridors.

18.	Blasting. Blasting is not allowed for any type of work in DHAI-R area.

19.	Disputes. No member (by virtue of one’s status) is allowed to stop the construction activity of other members. Any dispute / interpretation of Byelaws shall be referred to DHAI-R.

20.		Possession of Plots. Following procedure is laid down: -

a.	On clearing of all dues members should apply for possession of plots on prescribed form.

b.	A site plan indicating details (gate, manhole and water point location) shall be provided to the member.

21.		Preparation of Building Plans. For preparation of building plans (new or alteration) the member should engage a licensed architect and structural engineer on the panel of 
DHAI-R.

22.		Submission of Drawings. The member shall submit alongwith the application, three sets of drawings (in ammonia prints) duly signed and stamped by the DHAI-R registered Architect along with the soft copy covering following details: -

a.	Size of sheet should be 30x40 inches (Anx A) and all details be given at a minimum scale of 1 / 8 inch on same sheet.

b.	The plans of basement, ground floor and first floor, if any and the roof alongwith mumty.

c.	Front elevation, longitudinal section passing through stairs and site plan / key plan showing width of the road. In case of corner plot 2x elevations are required.

d.	Elevation and section of boundary wall, gate, ramp and water channel with respect to adjoining road / street.

e.	External dimensions of building.

f.	Internal dimensions of all rooms.

g.	The position and dimensions of all projections beyond the walls of the building.

h.	Roof plan showing the location / dimension of over head water tank, mumty.

j.	Total height of building with reference to reference point including level of finished floor and split-levels (levels be indicated on plans also).

k.	Location of reference service manhole and its invert level and location of water connection shall be clearly shown on submission drawing.

l.	Thickness and X-section of RCC structures.

m.	Location and size of overhead and underground tank.

n.	The sewerage line, waste water / soap line and drainage line should be laid independently and marked properly on the plan. The soap water should not be connected directly to the septic tank. It should be connected to the over flow manhole (constructed within the plot line) of septic tank. A water channel of 4x4 inches would be constructed along the main gate line. This drain would be suitably connected to over flow manhole of septic tank through a 1 inch dia pipe.

o.	Schedule of open / covered areas.

p.	Schedule of doors and windows.

q.	Covered area calculation block plan.

r.	Signature of Owner and the Architect on drawings along with required DHAI-R forms.

s.	Drawings must be of acceptable Architectural standards.

t.	Attested copy of ID Card, Allotment letter, Possession form, Site Plan, NOC form duly verified from Transfer & Record Directorate and Finance Directorate, 3x set of submission drawings (ammonia print), soft copy of drawing (in CD), bearing capacity report, duly signed undertaking by the architect and structural engineer on a prescribed form and prescribed dues (scrutiny fee water charges) as decided by DHAI-R from time to time.

u.	Soil test report duly signed and stamped by the DHAI-R registered firm along with 1xset of structural drawings on A3 sheet duly signed by the DHAI-R’s approved structural engineer along with the certificate on letter head that the structure is safe. These drawings showing layout and sectional details of foundations, beams columns, lintels, slabs, under ground and over head water tanks. This set of drawing is only for DHAI-R record and DHAI-R has no responsibility regarding the stability / safety of the structure. In case of commercial drawings, the structure should be duly vetted by the DHAI-R approved vetting engineer.

v.	Security charges as per DHAI-R’s approved rates. These will be refunded at the time of issuance of completion certificate.

w.	Isometric color view on a separate A4 paper with a soft copy (JPG).

23.		Approval of Submission Drawings. Following procedure will be followed:-

a.	The member will submit the plans with DHAI-R for approval as per DHAI-R Byelaws.

b.	Plans not conforming to DHAI-R Byelaws will be returned to the architect along with reasons by mail / may be collected by hand, otherwise member can collect approved drawing with permission letter and SOP for demarcation check within 15 working days.

c.	In case of observation on drawings the time for approval will be 15 working days after re-submitting the drawing after rectifying the observation.

24.	Revised Submission Drawing. If any change (demolition or addition) in the building plan is required, the revised drawing should be submitted for approval before making any changes. Member can collect approved revised drawing within 15 working days.

25.		Revalidation of Submission Drawing. The approved submission drawing is valid for three months and if construction of house is not started within three months than member will have to revalidate the drawing from DHAI-R after payment of prescribed charges.

26.		Oversight in Scrutiny of Drawings. Any oversight in the scrutiny of documents and drawings at the time of approval of the building plan does not entitle the member to violate the Byelaws.

27.	Demarcation of Plot. Demarcation of plot will be done when the submission drawings have been approved by building control section of TP & BC Directorate.

28.	SOP for Demarcation Check. Members are advised to follow steps given below for demarcation of plot before taking over construction and thereafter for confirmatory check by survey team of DHAI-R:-

a.	Step-I. Member to deposit the inspection chart with Town Planning Section of TP&BC Directorate and also provide the following items on the site at the time of demarcation:-

(1)	4 pieces of PVC 4 inch dia pipe 2-½ ft length each.

(2)	Cement, aggregate / sand / water etc.

(3)	Required labour with pick, shovel etc.

(4)	Pillars will be grouted / installed by the survey team in the presence of the owner / contractor which should not be disturbed or removed till the final demarcation of boundary wall upto DPC level.

b.	Step-II. Inspection Chart will be forwarded to Building Control Section for inspection of building construction

activities after completion of initial demarcation. Building Control Section has to ensure that the member gets the 2nd demarcation on lean after excavation of the boundary wall before starting of any construction activity on the inner building in case of no basement. However, in case of houses with basement member has to ensure demarcation on lean & DPC level of boundary wall whenever the basement is completed.

c.	Step-III. Before taking over the construction of boundary wall, the member must intimate TP Section for final demarcation on lean / DPC level. Town Planning as well as Building Control Section will also ensure that the plot is finally demarcated on lean / DPC level of boundary wall before taking any further construction.

d.	Note

(1)	The subject SOP is laid down for the convenience of members / contractors in order to avoid any violation / embarrassment at later stage. Please follow these SOP strictly otherwise the members will be held responsible of any violation.

(2)	Rs 1,000.00 (one thousand) and Rs 500.00 (five hundred) will be charged on revision of initial demarcation on the disturbance of pillars and issue of new Inspection Chart in case of loss respectively.

(3)	It is primarily the responsibility of member to ensure the inspection of work on each stage of construction as per Inspection Chart and signature of building inspector of DHAI-R. If any anomaly occurs on later stage, member will be responsible.

29.	Approved Drawings. The member / contractor must keep one set of approved drawings on site, which may be made available to DHAI-R staff during inspection. In case of non availability of approved drawings, fine would be imposed as per DHAI-R policy.

30.	Inspection during Construction.	It is the responsibility of the owner to get the site inspected as per the stages mentioned in inspection chart.

31.	Addition / Alteration. No construction, addition or alteration shall be allowed unless drawings are approved by DHAI-R. Any change after the approval of submission drawing will be regularized through submission of revised drawings.

32.	Construction without Approval. Any construction started / carried out without prior approval of authority shall be liable to be demolished (partly / wholly) with or without notice at risk and cost of owner.

33.	Duplicate Copy of Document/s. Copy of submission drawing / completion drawing / CD / soil test report may be given to owner (if available in record) by charging Rs 5,000/- for each document.

34.	Completion Plan. The member shall obtain the House Completion Certificate after rectifying the observations / violations (if any) within 90 days from the date of sending the violation notice by DHAI-R, failing which fine will be imposed as per DHAI-R fines. The documents to be attached with completion plan are as under:-

a.	2x set of drawings (ammonia print) duly signed and stamped by the registered 
DHAI-R Architect.

b.	Prescribed dues as decided by DHAI-R from time to time.

c.	Inspection Chart duly signed by the concerned Officer during construction.

d.	Soft copy of drawing.

e.	After the receipt of completion drawing, DHAI-R technical staff shall arrange to inspect such work and after inspection either approve or disapprove or regularize minor deviations with penalty at rates as approved by the DHAI-R from time to time.

f.	In case of no violation, completion case shall be put upto the DHAI-R Executive Board for final approval.

g.	In case of violation the member shall be asked either to pay the prescribed penalty against minor deviations or completion plan shall be returned unsanctioned with an order for demolition of the subject un-authorized construction.

h.	In case member intends to construct the building in phases, the sequence of construction in phases duly numbered shall be indicated on the submission drawing. For purpose of obtaining NOC of a building, the minimum requirement is completion of ground floor in all respect.

j.	If member wants to occupy the building partially / completely then he should submit an application for occupation of house. If member occupies the building without getting approval from DHAI-R penalty / fine would be imposed as per DHAI-R policy. Member can apply for completion certificate after occupying his house but completion certificate must be obtained within 3 years from date of approval of submission plan, failing which penalty would be imposed as per DHAI-R policy.

k.	Illegal occupants and violators will not be entertained with social & civic facilities of DHAI-R (i.e Jacaranda Club, Water bowzer, Ambulance, concession in Jungle restaurant, Car stickers and provision of cable network etc).

35.	Revised Completion Plan. If at any stage after the completion plan of building has been issued, any additions and alterations are made within the same building, approval of such revised completion plan from DHAI-R shall be mandatory.

36.	Cancellation of Completion Plan. If at any stage after getting completion a member found violating DHAI-R Byelaws:-

a.	He / she will be served three notices in a span of three months and completion will be cancelled after issuance of final notice.

b.	The fine of Rs 2,000/- month will be imposed starting one month after issuance of final notice till the removal of violations and applying for revised completion.

c.	If any member fails to pay the fine within specified time period and persistently violates the Byelaws, then DHAI-R reserves the right to disconnect / discontinue services till payment of fine and all the violations are rectified / cleared which will be verified by TP&BC Directorate.

37.	Imposition of Utility Bills. The utility bills will be issued as soon as member occupy / partially occupy the house or get the completion certificate.

CHAPTER-III

SPACE REQUIREMENT FOR BUILDINGS

1.		Residential Building Standards. All residential houses shall conform to following specifications / standards:-

| Area of Plot (Sq yds) | Allowable Covered Area (G.F) | Allowable Covered Area (F.F) | COS / Setback |
| --- | --- | --- | --- |
|  |  |  | Front (ft) | Rear (ft) | Side* (ft) | Side (ft) |
| Upto 200 | 85% (including car porch) | F.P of G.F Area | 5 | 3 | Nil | Nil |
| 201 to 249 | 75% (including car porch) | F.P of G.F Area | 7 | 3 | 3 | Nil |
| 250 to 399 | 70% (including car porch) | After leaving COS 90% of GF including car porch area OR FP of GF area less car porch | 10 | 3 | 3 | 3 |
| 400 to 600 | 68% (including car porch) |  | 15 | 5 | 5 | 5 |
| 601 to 800 |  |  | 18 | 5 | 5 | 5 |
| 801 and above | 60% (including car porch) |  | 20 | 5 | 5 | 5 |

Notes

a.	*Along car porch side.

b.	Front setback for standard plots may be relaxed upto 2 ft on payment of following regularization charges by the member:-

(1)	Upto 1 ft	-	Rs 1,00,000/-

(2)	Upto 2 ft	-	Rs 2,00,000/-

2.	General Conditions

a.	Covered Area

(1)	Shades shall not be counted in covered area.

(2)	In case of pergola, 25% of its area shall be counted for calculation of covered area. However, pergola shall not be permitted within the set-backs / compulsory open spaces.

(3)	The basement can be constructed 100% after leaving the COS.

(4)	Structures such as fiber glass, steel structure would be taken in the covered area.

b.	Basement. Generally open / closed basement is allowed to all members irrespective of topography of plots but with following conditions:-

(1)	In case of open basement or set-back is less than 5 ft an NOC is required from the neighbour who has an existing structure so that the area can be dug in till the boundary wall of his neighbour. No such NOC is required in case of closed basement.

(2)	Frontal set-back can be dug upto 3 ft only.

(3)	In case of any damage to the adjacent building, the owner of the plot and Structural Engineer / Architect shall be jointly responsible for such damages and shall have to use proper engineering techs in order to avoid damage to neighbouring buildings. DHAI-R in no way shall be held responsible for such damages.

(4)	The basement shall not be exposed more than 4 ft 6 inches from crown of the abutting road / zero level.

(5)	The side set-backs in open basement may be covered but there level should be maximum +2 ft from reference point.

(6)	Construction of ramp, stairs / steps leading to the basement is permitted within in the side and rear set-back without any super structure over them.

(7)	Clear height of the basement shall not be less than 8 ft 6 inches.

(8)	In all cases, the building should look like two storey and the total height of building from the reference point shall not be more than 37 ft.

(9)	Basement Wall / Retaining Wall adjacent to completed houses / endangering neighbouring structure should be completed within 15 days from the date of commencement of excavation.

(10)	All the retaining walls of the open / closed basement should be of RCC.

(11)	In case of open basement member can excavate 2 ft into the adjacent plot with the permission of the DHAI-R Building Control Section by acquiring NOC but the backfilling should be done with sand. In case, of adjacent house is constructed, the member would not be allowed to excavate.

(12)	If services, such as bath and kitchen etc are provided in the basement, the owner must provide mechanical disposal from the basement to the upper level in all cases (irrespective of levels of DHAI-R mains), so that there is no possibility of back flow in case of chockage of the sewer lines. DHAI-R will not be responsible for the consequences in any case.

(13)	Cost of additional services work shall be borne by the member.

(14)	The entry to the basement from rear and side set-back is allowed.

(15)	In no case the basement shall be allowed in the minimum prescribed set-backs.

(16)	Closed Basement, vaults, cellars and other structures, wholly or partly below the ground level / approach road level, shall be allowed provided minimum 
1 x emergency exit should be provided.

c.	Reference Point. Reference point shall be the intersection of gate centre line and reference road crown.

d.	Finish Floor Level. Finish floor / Plinth level of ground floor should not be more than 
4 ft 6 inches.

e.	Set-back Level. The level of set-backs should not be more than +2 ft but corner side set-back level may be raised upto level of adjacent road.

f.	Height of the Building & Height of Floors. Maximum height of the building including water tank / mumty or any structure should not exceed 37 ft from the reference point. In exceptional cases where site permits increase in height maximum upto 1 ft will be allowed after payment of Rs 15,000/- and approval from Competent Authority.

g.	No of Storeys. Maximum two storeys (ground + first) are permitted. Number of storeys will be counted from the reference street / road.

h.	Septic Tank. Septic tank should be constructed with their own RCC walls and should have a minimum distance of 3 ft from front boundary wall. Any other boundary wall should not be used for construction of septic tanks.

j.	Projection / Shade.  Sun shades to be kept as under:-

(1)	In front set-back not more than 3 ft.

(2)	In side set-backs not more than 2 ft 6 inches for plots equal to or larger than 400 sq yds and 1 ft 6 inches for plots below 400 sq yds.

(3)	In rear set-back not more than 2 ft 6 inches for plots equal to or larger than 400 sq yds and 1 foot 6 inches for plots below 400 sq yds.

(4)	Fiber glass coverage on window top to avoid direct sun or rain will be allowed only till width of window. Depth of such projections should not be more then 
2 ft 6 inches in side and rear set-back and 3 ft in front set-back for 400 sq yds and above plots. For plots less then 400 sq yds side shade width should not be more than 1 ft 6 inches.

(5)	No rooms shall be constructed on the projections / shades projecting beyond the building line.

(6)	Maximum fall of shade should not be more than 3 ft.

(7)	No projection beyond these limits weather permanent or temporary will be allowed in any set-back.

(8)	Design element on front / side shade (In case there is open space / nullah / road on that side) may be allowed at first floor to maximum allowable width of shade. No design element allowed on a side of neighbouring plot.

(9)	No other structure of any type is allowed in compulsory open spaces.

k.	Open Stairs Case

(1)	The plots having rear setback of 5 ft and more can have spiral stair in rear setback after leaving a clear distance of 2 ft 6 inches from rear plot line. Straight stairs having the width of 2 ft 6 inches also allowed in rear setback.

(2)	Open stairs are not allowed in side setbacks.

(3)	Mumty not allowed over open stairs.

l.	Mumty. Mumty conforming following specifications / conditions is allowed and may be used for storage / habitation with toilet whereas window(s) towards neighbouring plot / house other than staircase is / are not allowed:-

(1)	Location. Mumty can be constructed over primary (main) or secondary staircase (within the building line).

(2)	Width. Maximum width of mumty including design element shall not be more than half the average width of plot.

(3)	Height. Height of mumty including design element shall not be more than 11 ft from top of 1st floor roof slab. Additional 1 ft increase in height of mumty (maximum upto 12 ft), may be allowed on payment of regularization fee of 
Rs 15,000/-.

(4)	Covered Area. Covered area of mumty vis-à-vis area of under mentioned plot may be allowed as shown in front of each, whereas for plot having area 
in-between under-mentioned area, covered area of mumty will be calculated applying %age of lower side plot area:-

| Area of Plot (Sq yds) | % Age | Covered Area of Mumty (Sq Ft) |
| --- | --- | --- |
| 125 | 20 | 225 |
| 200 | 13.5 | 245 |
| 250 | 11 | 250 |
| 300 | 11 | 300 |
| 400 | 11 | 400 |
| 500 | 9 | 405 |
| 600 | 9 | 486 |
| 800 | 9 | 648 |
| 1000 | 9 | 810 |

(5)	Machine room for lift / elevator and design element will be part of mumty and its covered area will be included in covered area of mumty.

(6)	Shade / Projection. As per shades / projections of the building.

(7)	Structure(s) including raised solar panel(s) or geyser(s) on roof of mumty is / are not allowed.

m.	Entry Gate(s)

(1)	Position / Location of the gate(s) will be kept as per DHAI-R approved site plan part of the master plan.

(2)	Two gates shall only be allowed in case of corner plots or plots having roads on any two sides. Non-corner plots having frontage 70 ft and above can have two gates on front side but services such as transformer, DB, pole etc in front of second entry / gate will not be shifted. Charges for second gate on one side will be same as opening on two road charges.

(3)	Standard width of main gate including wicket gate and excluding pillars will be upto 20 ft and for corner plots width of 2nd gate is upto 14 ft. Width of gate pillars (inclusive of boundary wall) should not be more than 1 ft 6 inches, however width of main gate may be increased upto 25 ft after payment of regularization fee as mentioned in the fines. But services such as transformer, DB, pole etc falling in front of increased width will not be shifted. Increased width of gate if found in inches will rounded off and taken as whole foot on the higher side.

(4)	Provision of any type of arch / design element over the gate(s) is not allowed.

(5)	Wicket gate upto 3 ft width in extra land having opening on road is allowed conditionally that services such as transformer, DB, pole etc falling in front of second entry / gate will not be shifted. The gate size can be increased maximum upto 14 ft by paying charges @Rs 25,000/- per running foot. In addition, charges for gates opening on two roads OR having frontage more than 70 ft will also be applied. Maximum two gates including in extra land will be allowed.

n.	Ramp (Driveway) in Services Area. Ramp in front of gate in services area can be constructed subject to following conditions and specifications:-

(1)	For laying / rectifications of fault / re-laying of services including electricity, telephone, cables, gas, water supply etc four (4) beneath ramp minimum 6 inches dia independent conduits will be provided by the member.

(2)	Ramp at start of property / plot line should be maximum 18 inches high or at slope of 1:7 and its height will be taken from intersection of gate centre line & reference road crown. Profile / slope of the ramp should be as under:-

(a)	Where footpath does not exists, the ramp from property / plot line (gate) may be extended maximum upto the outer edge of storm water drain kerb stone along the road.

(b)	Where footpath exists, the ramp from property / plot line (gate) may be extended maximum upto the home-side (outer) edge of footpath / kerb stone.

o.	Size of Rooms. The minimum area of a room meant for human habitation shall not be less than 80 sft.

p.	Car Porch. Maximum size of car porches vis-à-vis plot area is as under:-

| Ser | Area of Plot (Sq yds) | Maximum Size including Side Setback |
| --- | --- | --- |
| (1) | Above 800 | 32 ft x 35 ft 18 ft x 18 ft (2nd Car Porch only for Corner Plots / Plots having opening on two roads) |
| (2) | 400 to 800 | 30 ft x 35 ft 18 ft x 18 ft (2nd Car Porch only for Corner Plots / Plots having opening on two roads) |
| (3) | 201 to 399 | 20 ft x 18 ft 12 ft x 18 ft (2nd Car Porch only for Corner Plots / Plots having opening on two roads) |
| (4) | Upto 200 | 14 ft x 18 ft 10 ft x 18 ft (2nd Car Porch only for Corner Plot / Plots having opening on two roads) |

Notes

(1)	Two (2) car porches shall be allowed for corner plots, plots with two entries and non-corner plots having frontage 70 ft and above.

(2)	Second car porch shall fall within the permissible projection / shade but with side car porch columns resting over the boundary wall.

(3)	Covered area of porch(s) shall be counted in the total covered area irrespective of its size / shape etc.

(4)	The distance of porch roof from boundary wall may be allowed as 5 ft and porch columns should be kept 8 ft from plot line.

(5)	For plots having area 250 sq yds and above porch columns shall have a clear distance of at least 8 ft from the outer edge of front boundary wall, however projection of 3 ft-wide towards front only is allowed.

(6)	For plots having area less than 250 sq yds porch columns shall not extend beyond the front building line, however projection from porch column towards front can extend upto 2 ft 6 inches.

(7)	The larger size porches can be constructed after leaving the COS.

(8)	Storm water from the roof of porch shall be drained within the plot.

(9)	For 200 & 125 sq-yards, porch columns shall not extend beyond the front building line, however, projection from porch column towards front only can be extended by 2 ft 6 inches.

(10)	High car porch is not allowed with columns resting over the boundary wall. They can however be permitted if kept clear of the COS.

(11)	Construction above / below the porch (basement) is allowed after leaving compulsory open spaces.

(12).	Gap above boundary wall upto roof level between porch columns may be covered with inward louvers / lattice / solid wall or Jali.

(13).	Design element on porch can be constructed upto the allowable width of building shade at front & sides. The design element should be without roof / pergola and it will not be counted in covered area. The design element can be constructed after approval from Competent Authority.

(14).	The min depth of porch for 1Kanal and above plots should be 15’ and less than 1 kanal plots is 12’.

q.	Boundary Wall

(1)  	Member can construct a boundary wall within his property line. If boundary wall of 4½ inches width is constructed then pillar of 9 inches x 9 inches at 10 ft distance must be provided. If member wants to construct a common boundary wall, approval of both neighbour should be necessary and affidavit in this regard from both neighbours to DHAI-R should be mandatory.

(2)  	Both neighbours shall have full right to use it on their respective sides / top. However, no space from right of way of road / street shall be utilized for this purpose.

(3)		Maximum height of rear boundary wall should be 6 ft above the level of rear road.

(4)		Maximum height of left / right / front side boundary wall should be 7 ft 6 inches from the highest point of the road in front of plot.

(5)		Minimum height of boundary wall should be such to ensure the privacy of the adjacent plot.

(6)		The boundary wall should be an RCC or brick masonry wall.

(7)		The front / side boundary wall (If there is open space / nullah / road on that side) may be constructed with grill or any other see-through material.

(8)		A safety grill upto 2 ft 6 inches can be provided above boundary wall.

(9)	If two adjacent plots are owned by single owner or different owners having blood relation (parents & their children, brothers and sisters or husband and wife) then the Boundary Wall between the two plots can be exempted / omitted subject to providing an application to DHAI-R by the owners (jointly) on Judicial Stamp Paper.

r.	Bay Windows.  For plots equal to or more than 500 sq yds, 2 ft 6 inches wide bay window and length 10 ft can be provided in frontal set-back. For plots less than 500 sq yds 2 ft 6 inches wide bay window can be provided in frontal set-back only. Area of bay window counted into total covered area. For plots having extra land up till 10 ft on rear or side bay window of 2 ft 6 inches width allowed on ground floor only.

s.	Parapet Wall. Parapet wall maximum upto 5 ft and minimum upto 2 ft 6 inches height may be allowed. However, height of parapet wall can be kept less than 2 ft 6 inches for design purpose only, provided that, that specific area of roof should be unapproachable in normal conditions.

t.	Main Stairs. Every building shall have a clear width of steps of stairs not less than 3 ft, with riser maximum upto 7 ft 6 inches and tread minimum upto 10 inches.

u.	Area of Servant Quarter. Area of servant quarter excluding toilet should not be less than 80 sq ft.

v.	Drain under Gate. A water channel of 4 inches x 4 inches would be constructed along the main gate line. This drain would be suitably connected to over flow manhole of septic tank through a 1 inch dia pipe. Steel grating shall be provided to cover it.

w.	Services Area in front of Plots. The member can develop the services area in front of his plot (a property of DHAI-R) as green area by confining it with edge stones having height of maximum 9 inches from footpath level or road level where no footpath exist. The height more than 9 inches may be allowed after obtaining approval of plan / scheme from TP&BC Directorate DHAI-R. Fencing / grills around services area is not allowed. Growing of flower plants / hatching upto 3 ft height is allowed except corner on road junctions.

x.	Electric Meters. Maximum two electric meters will be provided for each plot.

y.	Two Adjacent Plots. If member has two adjacent plots and he uses one plot for construction of his house and second as lawn, then he has to follow following procedure:-

(1)	Both the plots must be owned by the same member.

(2) 	If ownership is different then an affidavit on judicial stamp paper of Rs100/- and a sketch showing detail of boundary wall and gate duly signed by the approved architect will be required from second owner that he / she has no objection for utilizing his / her plot as green area only.

(3)	Members to get site plan / possession of the plot to be utilized as green / lawn.

(4)	Construction of under ground water tank and structure using steel, fiber or wood up till 25 ft x 25 ft in the plot utilized as green area will be allowed after approval from Competent Authority.

(5)	Sound proof generator may be placed after approval from Competent Authority.

(6)	Combine boundary wall will be erected and second gate is allowed on plot utilized as green area as per DHAI-R gate layout plan.

(7)	A passage / drive way from gate to building line would also be allowed, however no construction of any type such as porch etc would be allowed.

(8)	Monthly water charges will have to be paid by the owner.

z.	Extra Land

(1)	Construction in extra land without changing its category to constructable land is not allowed.

(2)	In case extra land is equal to or more than the respective set-back building line can be extended upto plot line.

(3)	Provision of gazebo / covered sitting area upto 150 sq ft using wood, fibre and / or iron will be allowed after leaving compulsory open space / set-back and approval from TP&BC Directorate DHAI-R.

(4)	Construction in extra land of Defence Villas will be decided considering the category of extra land on case to case basis.

(5)	Member holding extra land 10 marlas & above and maintaining it as green area will have to pay double water charges. After payment of dues, an additional water connection will be provided for green area.

(6)	DHAI-R reserves the right to retrieve or withdraw any extra land having category B or C allotted to the member and the amount paid for such extra land, if any, the same shall be reimbursed to the member. It is declared that extra land does not create any title or right in favour of the member since it is not the part of member’s adjacent plot as per member’s entitlement. Cost of any construction therein will neither be claimed by the member nor DHAI-R will pay.

(7)	Construction including water tank, septic tank and spiral stairs in non-constructable extra land is not allowed. However, with prior written approval by TP&BC Directorate DHAI-R shades as allowed in set-backs and perennial water tank having only one source of rainwater supply can be constructed.

(8)	Sound proof generator may be placed in extra land after approval from Competent Authority.

aa.	Construction Period. The member must complete construction on the plot within a period of 3 years from the date building plan is approved. In case of building is not completed within 3 years, penalty would be imposed as per DHAI-R policy.

bb.	Two Adjacent Plots at Different Levels. If two back to back / adjacent plots are at different levels and level difference is more than 5 ft then owner of the plot who first construct the house, will have to construct a common RCC retaining wall at rear side and foundation of RCC retaining wall should start from the lower road level.

cc.	Pools.  Swimming and decorative pools and fountains may be allowed after approval from Competent Authority. However, privacy of the adjacent houses should be ensured more over DHAI-R will not responsible for supply of water in case of swimming pool.

dd.	Water Tank

(1)	Under Ground Water Tank

(a)   Maximum size of water tank 1,500 gallons for plots upto one kanal.

(b)   Maximum size of water tank 2,000 gallons for more than one kanal.

(c)   Only one underground water tank is allowed.

(d)  Should have a minimum distance of 3 ft from front boundary wall and should be located in such a way that bowzer filling for water tank may be facilitated from the outside.

(e)	Tank should be constructed in RCC.

(f)	1 ft free float will be taken while calculating the capacity of water tank.

(2)	Over Head Water Tank

(a)   Maximum size of water tank 900 gallons for plots upto one kanal.

(b)   Maximum size of water tank 1,200 gallons for more than one kanal.

(c)    Height of water tank may be allowed upto 8 ft from roof top level.

(d)   Only one over head water tank (permanent / temporary) will be allowed.

However internal partitioning of tank is allowed.

(e)	Tank should be constructed in RCC.

(f)	1 ft free float will be taken while calculating the capacity of water tank.

ee.	Installation of Solar Panels. Solar panels / geysers on rooftop of residential / commercial building will be provisionally allowed and structures including raised solar panel(s) or geyser(s) on roof of mumty and / or overhead water tank are not allowed. DHAI-R reserves the right to change the policy, notify the member and the member will change accordingly within one month at his expense, risk and cost.

ff.	Generator.	Generator shall not be used as a prime source of electric supply. It may be used as standby with following conditions:-

(a)	Petrol or diesel driven generator with soundproof canopy may be installed.

(b)	Noise beyond the boundary limit shall not be allowed i.e noise control arrangement must be made.

(c)	Generator should be placed on rooftop (roof slab must be designed for structural stability to sustain the weight of generator) or in front lawn 5 ft away from common boundary wall. However, the generator shall not be placed in rear & side setbacks at ground floor and terraces at first floor.

gg.	Pipe Duct. Pipe duct upto 6 (six) inches may be allowed in COS / set-back.

hh.	Washing Area in Rear Set-back. One temporary shade of 7 ft x 4 ft will be allowed at rear compulsory open space (for laundry only).

jj.	Construction in Split Level. Due to variation in level or encountering hard strata, wherein excavation becomes difficult, split-level with a maximum of 3 ft level difference may be allowed.

kk.	Design Element in Setbacks. Design Element maximum upto 9 inches will be allowed in front setback and 6 (six) inches in sides / rear setbacks.

ll.	Features in Setbacks.

(1)	Rockery / water feature / flower pots upto height of boundary wall may be constructed with front boundary wall. In case rockery / water feature is provided along common boundary wall, a gap of minimum 6 inches shall be provided between the wall and rockery / water feature.

(2)	Rockery / water feature / flower pots in sides / rear clear open spaces may be allowed leaving clear passage of 2 ft 6 inches between building & rockery / water feature and minimum 6 inches gap between common boundary wall & rockery / water feature.

(3)	In case of seepage at the boundary wall of adjacent house due to the presence of rockery / water feature, the owner shall address the problem of seepage within 15 days from the issuance of notice from DHAI-R, otherwise, it will be rectified at owner’s risk and cost.

(4)	Plants are not allowed in side / rear set-backs.

mm.	Privacy

(1)	The pardah wall minimum upto 7 ft height in front of servant terrace / doors /  windows should be constructed with a non-see-through material such as fiber / steel / wood etc but not in brick or RCC wall.

(2)	Sill level of servant’s quarter window shall not be less than 5 ft. (if there is no pardah wall)

nn.	Miscellaneous

(1)	Earthing pit should be constructed inside the plot boundary.

(2)	Maximum width of stairs in side set-back leading to Ground Floor only should not be more than half width of set-back.

(3)	In case of violation, charges will be calculated across full length and not for a specific portion of violation.

(4)	Development / protection of plot (retaining wall etc) within boundary line including extra land is sole responsibility of owner.

(5)	Construction of boundary wall without construction of house and using it as green area / plantation of trees or any other purpose is not allowed.

(6)	Changing the colour of Distribution Board’s, Electric Panels and electric poles etc in service area is not allowed.

(7)	No structure of any kind will be allowed on roof except mumty and 1 x OHWT.

(8)	Relocation of Plots. DHAI-R reserves the right to relocate / cancel the location and dimensions until physical possession (demarcation) of the plot is given.

3.	Commercial Building Standards. Commercial plots shall observe the following standards:-

| Area of Plot Sq Yds | Foot Print | Arcade at GF | COS (Width in ft) | Floors |
| --- | --- | --- | --- | --- |
|  |  |  | Front (ft) | Rear (ft) | Sides (ft) |  |
| Upto 100 | 100% | - | - | - | - | B+G+3 for Sectors Commercials B+G+5 Main Commercials |
| 101 to 250 | 100% | - | - | - | - | B+G+3 for Sectors Commercials B+G+5 Main Commercials |
| 251 to 400 | 90% | 6 ft | - | 7 ft 6 inches | - | B+G+3 for Sectors Commercials B+G+5 Main Commercials |
| 401 to 600 | GF = 85% Above GF = 75% | 6 ft | - | 7 ft 6 inches | 5 ft @ | B+G+3 for Sectors Commercials B+G+5 Main Commercials |
| Above 600 | Will be decided by the Competent Authority |
| @ Note: One side. a. Smaller plots amalgamated into one larger plot up till 400 sq yds will follow Byelaws of smaller plot. b. In case a commercial plot falls in residential area then set-backs and building height of residential area will be followed. |

4.	General Conditions for Commercials

a.	Height

(1)	Main Commercial. Maximum height of the building may be increased to 
77 ft from reference point including machine room for lift, water tank and stair mumty.

(2)	Sector Commercial. Maximum height of the building may be increased to 
55 ft from reference point including machine room for lift, water tank and stair mumty.

(3)	For Larger Commercial Plots. DHAI-R will give separate approval depending on nature of commercial project.

b.	Height of Floor and Area of Shops. The height of floor should not be less than 9 ft. Minimum area of the shop should not less than 100 sft.

c.	Basement. Basement is allowed to all members irrespective of topography of plots but with following conditions:-

(1)	In case of open basement, an NOC is required from the neighbour who has an existing structure so that the area can be dug in till the boundary wall of his neighbour. No such NOC is required in case of closed basement. In case of any damage to the adjacent building, the owner of the plot and Structural Engineer / Architect shall be jointly responsible for such damages and shall have to use proper engineering techniques in order to avoid damage to neighbouring buildings. DHAI-R in no way shall be held responsible for such damages.

(2)	The basement shall not be exposed more than 4 ft 6 inches from crown of the abutting road / zero level.

(3)	Clear height of the basement shall not be less than 8 ft 6 inches.

(4)	Basement Wall / Retaining wall adjacent to completed houses / endangering neighbouring structure should be completed within 15 days from the date of commencement of excavation.

(5)	If services, such as bath and kitchen etc, are provided in the basement, the owner must provide mechanical disposal from the basement to the upper level in all cases (irrespective of levels of DHAI-R mains), so that there is no possibility of back flow in case of chockage of the sewer lines. DHAI-R will not be responsible for the consequences in any case.

(6)	Cost of additional services work shall be borne by the member.

(7)	Construction of RCC retaining wall (as per structural design) at building line shall be compulsory.

d.	Reference Point.  Reference point shall be the intersection of building centre line & reference road crown.

e.	Projection / Shade

(1)	Maximum 3 ft beyond plot line at front and rear (if site permits).

(2)	Conversion of projections into habitable area only at front. However, rear may be used for balconies only.

(3)	Corner plots or plots having opening on two roads would be allowed construction on shade at front and side / rear provided that dues for corner / opening on two roads are paid. Plots which have openings on three sides the construction on shade at 3 sides shall be allowed after paying double the charges for corner plots.

f.	Mumty. Maximum upto 30% of the plot area can be utilized for mumty. Extra 20% can be constructed by paying Rs 2500/- per sft additional charges on this account. Mumty area may be used for machine room, lift room, generator room, living area or bathrooms.

g.	Arcade. The commercial plots upto 250 sq yds can be constructed with or without arcade.

h.	Entrance Steps. Entrance steps can be provided upto the 3 ft out side the plot line.

j.	Septic Tank.  A septic tank of size 3 ft x 5 ft x 5 ft can be constructed adjacent to the entrance stairs in the parking area. To maintain the Septic Tank and to keep it clean and workable is the responsibility of the plot owner.

k.	Shops / Offices / Apartments Numbering.  Shop / Office / apartment number will be shown on submission drawing for reference. The numbers will be in clockwise direction following the suffix B1, B2, G, F1, F2, F3, F4, F5 and so on e.g Shop / Office / apartment number in basement next to Ground Floor will be numbered as 1B1, for 2nd basement 1B2, Shop / Office number 1 on G.F will be named as 1G, Shop / Office / apartment number 1 on First Floor will be named as 1F1, for second floor 1F2 and so on.

l.	Partial Selling of Shops / Apartments / Offices. The partial selling of units like shops, apartments or offices is allowed after completion subject to the following: -

(1)	The shop numbers should be properly marked in submission / completion drawing as per the procedure laid down in DHAI-R Byelaws.

(2)	The partial selling should be through DHAI-R 
(Transfer & Record Office) after payment of prescribed dues.

(3)	In case of partial selling 20% of the shops should be kept by the owner excluded mumty. However member can sell a whole plaza to a single owner.

(4)	All the responsibilities for the provision / maintenance of services such as Electricity, Sui Gas, Water, Telephone, Cable, Fire-fighting, Security, structural safety etc would be the sole responsibility of the owner of the plaza.

(5)	No good will / Pagri is allowed, failing which will result in heavy fines / disconnection of services.

(6)	In case of any structural change prior approval from DHAI-R is mandatory. However the internal / soft partitioning can be done without approval.

m.	Occupation. Any commercial unit like shops / offices / halls / apartments can be occupied after completing the front façade of the whole building and the floor to be occupied should be completed in all respect. However, completion certificate should be obtained within 3 years from the date of approval of first submission drawing.

n.	Finish Floor Level. Finish floor / Plinth level of ground floor should not be more than 
4 ft 6 inches.

o.	Hoardings

(1)	The content of display has to be approved by DHAI-R before hand and payment of fee as prescribed by Authority from time to time.

(2)	Fixing arrangement like hooks etc should be planned adequately.

(3)	On the facia of shop 2 ft wide space be provided to fix hoardings.

(4)	For the visual display hoardings large screen TV has to be in such a place so that attention of the drivers is not distracted.

(5)	Sound is not allowed in advertisement.

(6)	Electrical & Structural responsibility of neon signs shall be of the owner.

(7)	The name of the owner, mobile number and address has to be displayed on the side of his / her hoarding.

(8)	Any hoarding at any time can be dismantled by DHAI-R.

(9)	The size, shape, weight, look, structure stability and electrical safety to be submitted to DHAI-R for approval of the large hoarding are the responsibility of Civil / Mechanical Engineer.

p.	Stair Hall

(1)	The clear width of stairs shall not be less than 3 ft. The riser shall not be more than 7 inches and the tread shall not be less than 10 inches.

(2)	Not to be constructed with inflammable material.

(3)	All stair cases should be of RCC.

(4)	Walls to be made in RCC and with fire rated doors having fire rating of 3 hours.

(5)	All stair halls have to be connected with the basement and the roof top.

(6)	The minimum clear head room under beams and stair landing shall be 7 ft.

q.	Lightening Protection. For all commercial buildings lightening protection should be provided.

r.	Façade Code

(1)	Maximum effort to make the elevation in uniformity.

(2)	Module of pillars / column with equal openings and the size of columns are the same.

(3)	Drainage of storm water will not be through spouts but through down pipes.

(4)	No sanitary pipes services for kitchen as well as bath rooms be allowed on the face of the shop.

(5)	AC heat exchangers, services pipes, electrical cables, telephone cables and dish cables are not allowed on the face.

(6)	Passages for all the above services have to be provided in design.

(7)	Advertising hoardings has to be designed and uniformity has to be observed.

(8)	If the face is glass cleaning trolley and trolley rail has to be provided.

(9)	Services not to be exposed.

(10)	False ceiling, night lighting, cleaning in front of the shop in the corridor or arcade is the responsibility of the shop owner.

s.	Commercial Signage

(1)	Width – Complete front face of the shop.

(2)	Depth – Standard 1 foot.

(3)	Height – Upto 3 ft.

(4)	Corner shop with exterior side face shall be allowed signage over the window width with height not exceeding 5 ft.

(5)	Placement of any other Temporary / Permanent materials outside the shopping centre is strictly prohibited.

(6)	Safety of signboard to avoid any incident / injury to any visitor will be sole responsibility of owner / member.

t.	Provision for Special Persons

(1)	Minimum one toilet for handicapped equipped with special fixtures.

(2)	Minimum one lift in all commercial and public buildings, which can accommodate a wheel chair.

(3)	Ramp from footpath level to entrance of the building.

u.		Commercial

(a)	Petrol or diesel driven generator with soundproof canopy may be installed.

(b)	Noise beyond the boundary limit shall not be allowed i.e noise control arrangement must be made.

(c)	Generator should be placed on roof top only (roof slab must be designed for structural stability to sustain the weight of generator).

v.	Toilets

(1)	Be provided in each commercial block.

(2)	Separate arrangement for ladies is mandatory. One WC for the disabled is encouraged.

(3)	Cleaning and maintenance of the toilets is the responsibility of the owner.

w.	Lifts. Lifts / Escalator shall be provided in building where the climb is more than four storeys (Ground Floor + 3) & shall conform to the latest technical provision.

x.	Swimming Pool. No swimming pool can be provided for plots upto 600 sq yds. For Plots more than 600 sq yds the swimming pool can be constructed after the approval of DHAI-R Competent Authority.

y.	Installation of Antenna Tower & Lightening Conductor

(1)	Permission for Installation of Antenna Tower & Lightening Conductor will be valid for one year, which may be renewed every year with prescribed fee.

(2)	The position of the tower has to be incorporated in design of the building the weight and placement has to be taken care of in the building structure.

z.	Tandoor and Flour Grinding Machine

(1)	Permission for fixing is essential from DHAI-R.

(2)	No wood as fuel will be used.

(3)	Flour grinding machine is not allowed also industrial and semi industrial activities are not allowed.

aa.	Fire Safety and Security System

(1)	Width of stair flight shall not be less than 3 ft 6 inches.

(2)	Stair hall shall have concrete walls.

(3)	Stair hall doors shall have fire rating of 3 hours.

(4)	All building shall be equipped with fire hose and GI / CI exposed pipes painted in red with fire fighting wall cabinets on each floor. The length of the pipe should cover a whole floor area.

(5)	Fire extinguishers should also be provided on each floor.

(6)	Separate fire motor shall be installed in the basement.

(7)	Steel structure shall have a fire safety of 3 hours and ½ hour for non structural members.

(8)	State of the art security system, approved by the Authority shall be mandatory for all building constructed in DHAI-R.

bb.	Parameters for Educational Institutions

(1)	Parking Space. All educational institutions shall leave 20 ft wide parking space in addition to the space (ROW) on all the side of their leading roads. Parking shall also be provided in the basement for vehicles of the staff as approved by the Authority.

(2)	Clear Space.  All educational institutions shall leave 30 ft clear space at front whereas 10 ft space at other three sides between the compound wall and the building directions.

(3)	Ventilation. Each classroom should have at least two doors, one on each end for better and free ventilation. Adequate cross / forced ventilation shall be provided at opposite directions.

(4)	Lavatories. An adequate number of lavatories should be provided at each floor.

(5)	Water Points. Electric water cooler shall be provided on as required basis.

(6)	Residential Accommodation. No residential accommodation shall be built for the staff in the premises allocated for institute. However, guardrooms may be constructed in the premises with the approval of the Authority.

(7)	Height of Rooms. Minimum of 12 ft clear height shall be provided for main rooms such as classrooms, laboratories, etc. The clear height of these rooms may be 10 ft if air-conditioning is proposed and implemented.

(8)	Master Plan. School administration shall submit a Master Plan of the use of space even if they may not be interested to construct the total area initially. The Master Plan shall clearly indicate the playing areas, which shall never be utilized for construction purposes. The assessment of such areas shall be made keeping in view the standard sizes of playground for various games.

(9)	Minimum Height. Minimum height of the educational institutions shall be restricted to 44 ft with three storey if it is constructed in area other than residential area, whereas it shall be 30 ft with two storey in residential area.

(10)	MI Room. A room for medical treatment shall be provided.

cc.	Structures on Roof. Only the following structures of permanent nature may be constructed on roofs provided they are designed and built to the satisfaction of the Authority: -

(1)	Chimneys / air conditioning and other ducts, vents and wind catchers.

(2)	Water tank suitably designed.

(3)	Radio and television antenna post.

(4)	Parapet walls of 3 ft height. In case of accessible roof, the provision of railing parapet wall would be compulsory.

(5)	Staircase tower (mumty).

(6)	Lift rooms, Sky light etc.

(7)	Other structure, which the DHAI-R may permit by general or specified order.

(8)	No mobile phone antennas and billboards are allowed on roof of house for residential plot, however, allowed for commercial subject to approval of Authority.

dd.	For Amenities and Commercial

(1)	On completion of construction and before main electrical connection is provided to the building / house, the member shall submit test report of electrical system issued by a government / WAPDA approved wiring Inspector.

(2)	An independent earth pit will be provided in the building / house. The earth resistance of the pit must be less than 5 ohms.

ee.	Instructions for Shop Owners

(1)	Garbage shall not be thrown in front of houses / shops / public buildings. Shopkeepers shall place dustbin in front of their shops and place the garbage in dustbin from where it shall be picked up by Authority.

(2)	In order to avoid inconvenience to the customers, air conditioners shall be installed at the height of 8 ft from the level of veranda and proper arrangements shall be made for drainage of water. Preferably split type of air conditioners may be installed.

(3)	Wall chalking, writing on walls and pasting of posters etc on the walls shall not be allowed.

CHAPTER-IV

HEALTH AND SAFETY GUIDELINES

1.	Architect and engineers should make sure safety of the building by practicing proper engineering technique, professional skills and execution procedures as per health and safety standards.

2.	Architects, engineers and other professional persons involved in design of building should make sure not to include anything in the design that would necessitate the use of unwarrantably dangerous structural procedures and undue hazards, which could be avoided by design modifications.

3.	Every member, contractor and sub-contractor shall make an arrangement during operation, handling, transport, storage of building material to ensure the safety and health of the labour and public.

4.	Every member, contractor and sub-contractor shall ensure that all workers are properly informed of the hazards of their respective occupations and the precautions necessary and adequately supervise to avoid accidents, injuries and risk to health, in particular that of young workers, newly engaged workers and illiterate workers.

5.	Blasting and use of explosives for excavation / demolition is not allowed.

6.	Debris shall be handled and disposed off by a method, which will not endanger workers and public safety and health.

7.	No youth under the age of 14 is permitted on the habitat construction site.

8.	Use of ladders is not allowed during poor weather or on windy days.

9.	Safety of worker, labour and visitor will be sole responsibility of member / owner.

CHAPTER-V

ADMINISTRATIVE ASPECTS

1.	Commercial Activity. No commercial / semi commercial activity is permitted in the residential area.

2.	Messes / Guest Rooms. Residential accommodation can not be used / rented as Mess, Guest House, Guest Room or Hostel etc.

3.	Utilization of Vacant Plots. Vacant plots / open area can not be used for any function / gatherings except funeral gathering.

4.	Fire Works / Discharge of Arms. To guard against any untoward incident, display of fireworks (Aatish Bazi) and discharge / testing of arms is prohibited in residential area.

5.	Distinctive Marking / Flags. Flags / Banners which show Political / Religious / Sectarian affiliations are not allowed on both residential and commercial buildings.

6.	Grave Yard.  DHAI-R policy on grave yard will be followed strictly 
(aval with Admin Directorate).

7.	Noise Pollution. No person shall make, cause or permit to be made any noise or sound which disturbs or tends to disturb the serenity, peace, rest, enjoyment, comfort or convenience of the neighbourhood or of persons in the vicinity. DHAI-R considers that the acts listed below cause noises or sounds which are objectionable:-

a.	Playing or operating any radio, stereophonic equipment, television receiving set or other instrument or any apparatus for the production or amplification of sound, where the noise or sound is clearly audible at a point of reception in a residential area.

b.	Harbouring or keeping any animal or bird which persistently cries, barks or howls.

c.	Idling running of a machine for more than 15 minutes.

8.	Hiring of House. Any tenant hiring the house will get an NOC from Security Directorate of DHAI-R.

9.	Security Check Post. Security Check Post within plot line upto maximum 5 ft x 5 ft will be allowed after approval from Competent Authority. No check post will be allowed out side.

10.	Vehicle Stickers. All the members residing in DHAI-R are bound to get their vehicles stickers from Security Directorate of DHAI-R after filling requisite forms (available with Security Directorate).

11.	Rash / Un-safe Driving. All the residents are requested to drive within allowable limits in DHAI-R. Driver caught over speeding / un-safe driving will be liable to traffic laws. Underage driving strictly prohibited. Similarly driving a motorbike without safety helmet is not allowed within DHAI-R premises.

12.	Servant Passes. Member should get passes for all servants from Security Directorate.

13.	Hazardous Materials / Chemicals. Storage of any kind of hazardous materials / chemicals in residential / commercial buildings is strictly prohibited.

14.	Business Activities in DHAI-R. Permission for commencing any business activity in DHAI-R MUST be obtained from Marketing Directorate as per the “Business & Placement Form”. Form is available in Marketing Directorate.

CHAPTER-VI

CONSTRUCTION BYELAWS

1.	The temporary store would be constructed within the plot or in the adjacent plot without tempering the plot and with the permission of DHAI-R Building Control Section.

2.	The construction material would be placed within the plot area or in the adjacent plot without tempering the plot and with the permission of DHAI-R Building Control Section.

3.	Every person undertaking building work shall provide adequate readily accessible sanitary conveniences for all persons engaged on that work. The sanitary convenience provided shall be sited in such a position as not to create a nuisance or cause offence to persons, either in a public place or to persons residing or working in any premises adjacent to or near the site where building work is being undertaken. The sanitary convenience provided would be disposed off to DHAI-R sewer through septic tank. No direct disposal of sewage to main sewer would be allowed.

4.	In case of open basement 2 ft excavation in the adjacent plot can be done with the permission of owner / DHAI-R Building Control Section provided the backfilling would be done with sand and the retaining wall would be constructed within 15 days from the commencement of excavation.

5.	Any dust produced as a result of construction must be kept to a minimum by damping down with water. Stockpiles of materials must be kept damp to prevent windblown dust.

6.	Screen the whole site to stop dust spreading. Cover piles of building materials like cement, sand and other powders, regularly inspect for spillages and locate them where they will not disturb the adjacent constructed house / s.

7.	Collect any waste / water generated from site activities in settlement tanks, screen, discharge the clean water and dispose off remaining sludge at appropriate location.

8.	No burning of materials on site.

9.	No body would be allowed to wash any type of vehicle on road or ramp outside the building. If any body violate it, fines would be imposed as per DHAI-R policy.

10.	No noise emitting equipment such as wood / steel cutting machines, marble cutters / grinders can be placed in porch / lawn or out side the building.

11.	Provide, fix and maintain suitable screens or awnings to screen the building and scaffold so as to effectively minimize dust and debris from falling or being blown over the boundaries.

12.	During the construction activities like cutting / grinding of marble, cutting of wood, steel etc cover the outer openings such as doors, windows ventilators etc. with polythene sheet to avoid spreading of dust into the adjacent houses.

13.	The working hours for construction activities would be as under:-

a.	upto 1900 hrs in winter.

b.	upto 2100 hrs in summer.

14.	Debris shall not be allowed to accumulate so as to constitute a hazard.

15.	All roads, sidewalks and the thoroughfares bordering on or running through any 
excavation site shall be provided with substantial guard-rails or board fences.

16.	Under ground water tanks shall be covered / bounded by a 4 ft high safety grill / parapet during construction.

17.	During darkness, all public sidewalks shall be adequately illuminated and warning lights or flares shall be placed upon the property to ensure safety of pedestrian and vehicular traffic.

18.	If the member violates the Byelaws and does not rectify or remove the violation in accordance with the Byelaws within specified time frame then the remaining work will be allowed after rectifying the violated work.

19.	In case of continuous persistence of violation despite three notices DHAI-R reserves the right to take necessary action / rectify at the member’s risk and cost.

Annex-B

FINES CHARGES

| a. | Excessive excavation / construction without approval of drawing / Initial demarcation. | Rs. 25,000/- |
| --- | --- | --- |
| b. | Excess Building Height. Upto 37 ft is allowed in Byelaws, 1 ft additional height can be regularized with fine of Rs.15,000.00. Exceeding this limit will be demolished at owner’s risk and cost. |
| c. | Excess Projection of Shades. Maximum upto 6 inches deviation from the Byelaws will be allowed with a fine of Rs.1,000 / Sft. Exceeding this limit will be demolished at the owner’s risk & cost. |
| d. | Construction at Side / Rear set-back maximum upto 6 inches. | Rs. 1,000 / Sft |
| e. | Construction at front set-back i.e. column / porch area maximum 6 inches. | Rs. 2,000 / Sft |
| f. | Non provision of screen towards neighbouring house/s. | Rs. 5,000/- |
| g. | Members tempering with main sewer line. | Rs. 10,000/- |
| h. | Members tempering water supply line. | Rs. 10,000/- |
| j. | Removal / shifting of demarcation pillars. | Rs. 1,000/- |
| k. | Illegal occupation / occupation without approval of DHAI-R. | Rs. 15,000/- |
| l. | Damages to DHAI-R road / footpath & services. Repair of damage will be carried out at the defaulters risk and cost. | Rs. 5,000/- + Actual cost of repair |
| m. | Damage to neighbour’s structure. | Rs. 10,000/- + Actual cost of repair / construction |
| n. | Wastage of water i.e. overflowing from underground water tank, car washing on ramp / porch / road and water tap opened freely. | Rs. 5,000/- |
| o. | Illegal water connection (installation of pump / motor). | Rs. 10,000/- |
| p. | Dumping of material on road / shoulder and blockage of drain. | Rs. 5,000/- +Shifting charges |
| q. | Cutting of steel / mixing of mortor on road / street. | Rs. 5,000/- +Cost of repair |
| r. | Dumping of debris / waste material / garbage on un-auth places. | Rs. 5,000/- +Shifting charges |
| s. | Cutting of road without the permission of DHAI-R. | Rs. 10,000/- +Cost of repair work |

| t. | Commercial activity in residential area. | Rs. 2,00,000/- |
| --- | --- | --- |
| u. | Unauthorized / illegal construction at roof top maximum upto 50 sqft (Residential). | Rs. 1,000 / Sft |
| v. | Unauthorized / illegal construction at roof top maximum upto 50 sqft (Commercial). | Rs. 2500 / Sft |
| w. | Extension of shade maximum upto 6 inches (Commercial) | Rs. 10,000 / inch |
| x. | Increase in height of ramp upto 6 inches from prescribed limit. | Rs. 20,000/- |
| y. | Un attended underground water tank against hazards. | Rs. 10,000/- |
| z. | Construction not completed in 3 yrs from first approval of submission drawing (Residential). | Rs. 1,000/- Per Month |
| aa. | Construction not completed in 3 yrs from first approval of submission drawing. (Commercial). | Rs. 2 / Sft Per Month. After three years |
| bb. | Occupation of any floor / floors without approval. | Rs. 5 / Sft Per Month from the date of occupation |
| cc. | Illegal use of electricity / water. | Rs. 20,000/- |
| dd. | Increase in height of boundary wall maximum upto 9 ft. | Rs. 200 / sft |
| ee. | Increase in height of parapet wall maximum upto 6 ft. | Rs. 200 / sft |
| ff. | Improper signage and misuse of circulation spaces. | Rs. 5,000/- plus confiscation of the signboard/hoarding/ unauthorized material |
| gg. | Increasing the size of overhead / underground water tank maximum upto 250 gallons. | Rs. 200 / Per Gallon |
| hh. | Increase in width of wicket gate in extra land. | Rs. 25,000 / Rft |
| jj. | Completion not obtained within 90 days from date of 1st violation notice (Residential). | Rs. 1,000 / Per month |
| kk. | Completion not obtained within 90 days from date of 1st violation notice (Commercial). | Rs. 2,500 / Per month |
| ll. | Increase in width of main gate maximum upto 5 ft from the allowable limit. | Rs. 3,000 / Rft |
| mm. | Revalidation of drawing if construction not started within three months. | Rs. 5,000/- |
| nn. | Increasing width of mumty maximum upto 2 ft. | Rs. 1,000 / Per inch |

Note: Violation beyond the prescribed fines should be demolished.

# Text boxes

Anx-A

SHEET SIZE 30 x 40 inches